## Slide 1: Laundry Now
Senior Design Project Proposal Submitted By:
Frank Monforte, Ryan Russell
Sonoma State University Department of Engineering Science
Advisor: Dr. Farid Farahmand
Client: Tramaine Austin-Dillon
SSU Residential Area Coordinator – Sauvignon Village East
laundrynowssu.weebly.com
laundrynowssu@gmail.com

## Slide 2: Overview
Problem and Solution
General System Overview
In Depth System Description and Technical Components
  Sensors, Controllers, Server
Testing and Results
Materials and Costs
Timeline
Potential Risks
Conclusion

## Slide 3: The Problem
6 Million People in California Living in Aparments.
No Way to Determine if Wahers or Dryers are Available for Use Without Making a Trip to the Laundry Room
Difficult for Management to Keep Track of Which Machines are Being Used the Most (Maintinence and Repairs) and Which Machines May be Broken Down

## Slide 4: The Solution
Design an easy to install, inexpensive monitoring system that allows users to check the status of machines in the laundry room. Include usage count so management can see which machines are being used the most (maintinence and repairs).
Simple for Residents to Use and Reliable
Expandable Based on Number of Machines
Non-Invasive Design
Inexpensive to Purchase and Install
Allow Property Management to Track Machine Use

## Slide 5: Existing Products
LaundryView by Mac-Grey Corp.
  Designed To Work With Their Supplied Washers/Dryers
  Allows Users To See What Machines Are Running/Time Left
  Costly, Requires Wi-Fi Enabled Washers/Dryers
Remote Laundry Monitoring System by LG
  Invasive (Modems Need To Be Installed On Machines)
  Only In Home
  Requires An Extra Plug In Unit

## Slide 6: Basic Implementation

## Slide 7: System Overview
3 Main Components
  Server, Controller Node, Sensor Node
Sensor Node on Each Washer/Dryer
Sensor Nodes Connected to Controller Node
  Up to 8 Sensors per Controller Node
Each Controller Node Connected to a Server
  Up to 4 Controller Nodes per Server
Server Connected to LAN via Wi-Fi

## Slide 8: Design

## Slide 9: Design Challenges
SPI & I2C Communication Interfaces
  Addressing challenges
  Minimize Cost, Maximize Versatility
Simple, Easy to Install and Manage
  Store Data Internally
  WiFi Network Connected
Power Supply
  Single Power Supply for entire system

## Slide 10: Demo Unit
1 Server
2 Controller Nodes
4 Sensors Nodes
  2 Sensor Nodes per Controller Node

## Slide 11: Sensor Node
Digital 3-Axis MEMS Accelerometer
Analog Devices ADXL345 Chip
SparkFun Breakout Board
SPI Interface
Sensor Node Select Chip (Demultiplexer)
  NXP Semiconductors 74LV138N IC

## Slide 12: Sensor Node to Controller Node Communication

## Slide 13: Sensor Node to Controller Node Circuit

## Slide 14: Sensor Select Chip - Demultiplexer
Sensor Select Chip allows less wires to control accelerometers over the SPI interface
NXP Semiconductors 74LV138N IC
3 Input Lines (3 Wires)
8 output options (Up to 8 Sensor Nodes)

## Slide 15: Controller Node
Manages Data from Sensor Nodes
  Each Sensor Node Checked Individually
Multiplexed SPI Chip Select Lines
  Standard Data SPI Data Transfer from Master (Controller Node) to Slave (Sensor Node)
  3 Chip Select Lines to Control up to 8 Devices
Data Retrieved by Server over serial UART connection

## Slide 16: Server to Controller Node Communication

## Slide 17: Controller Node to Server Circuit

## Slide 18: Server
Digilent ChipKIT WF32
  Integrated Microchip PIC32MX69F512L MCU
  Integrated Microchip MRF24WG0MA WiFi Controller
  Built in PCB Antenna (on WiFi Controller)
Server Manages Communication with Controller Node
Washer/Dryer Status and HTML File Stored on Server
WiFi Controller Handles Communication between server and LAN (SPI)
  WPS Enabled, 802.11b/g, 5Mbps
WEP, WPA, WPA2-PSK Capable

## Slide 19
Movement Data Collected By Controller Node from Sensor Node (5 Min)
Controller Node Analyzes Movement Data
  Makes Best Determination If The Washer/Dryer is:
    Running
    Completed a Cycle
    Empty
Server Gathers Data From Controller Nodes (5 Min)
Server Updates Webpage HTML File
Server Sends Latest HTML File To User When Requested (Wi-Fi)
Result

## Slide 20: User Interface

## Slide 21
Server Flow Diagram

## Slide 22
Controller Node Flow Diagram

## Slide 23: Sensor Test Results
Parallax 2-Axis MEMS Accelerometer
Digital Output to Arduino Uno
Data sent serially to laptop
Data Points plotted in MATLAB
Results analyzed

## Slide 25
Potential Risks
Some Washer/Dryer Machines May Not Be Compatible
  Washer/Dryer Too Quiet – Unable To Collect Sufficient Movement Data
  Stacked Washer/Dryer Units – Unable To Differentiate Between Machines
Signal Degradation Between Sensors
  Long Wire Distances May Cause Data/Clock Signals To Degrade
  May Need To Add Distance Limitations
  Add Buffers To Isolate Signal Between Sensor Nodes/Controller Nodes

## Slide 26: Estimated Budget

## Slide 29: Project Milestones

## Slide 30: Supporting Courses
Programming (CS115)
Fundamentals of Logic Design (ES112)
Digital Logic Design (ES210)
Advanced Programming (ES314)
Microprocessor and System Design (ES310)
Wireless Communication (ES485)
Intro to Networking (ES465)

## Slide 31: Questions/Comments
laundrynowssu.weebly.com
Laundry Now
Senior Design Project Proposal Submitted By:
Frank Monforte, Ryan Russell
Sonoma State University Department of Engineering Science
Advisor: Dr. Farid Farahmand

## Slide 32: References
http://www.macgray.com/
Mac Gray is the inventor and supplier of LaundryView and all of the products needed to run LaundryView. 11/15/2014
http://www.campus-solutions.net/index.html
Campus-solutions is one of the many features that is offered by Mac Gray. This website shows how LaundryView has been implemented in Colleges across the country and how it has improved the efficiency of college laundry facilities. 11/15/2014
http://www.amazon.com/LG-Electronics-RLM20K-Laundry-Monitoring/dp/B0012OMY2K
Is the main selling source for LG’s Remote Laundry Monitoring System, provides cost along with description of what the product does and some reviews form customers. 11/15/2014
http://www.maytag.com/Laundry-1/Laundry_Laundry_Appliances_Washers-3/102120050+4294966015/
Provides the estimated cost of the Maytag washers and dryers that Mac Gray offers as part of their laundry facility service, and the machines needed to allow for the use of LaundryView. 11/15/2014
http://www.nmhc.org/Content.aspx?id=4708
This link provides the number of residents the live in apartment complexes in the state of California and the whole country. 12/4/2014

## Slide 33
http://www.analog.com/static/imported-files/data_sheets/ADXL345.pdf
Analog Devices ADXL345 Data Sheet. 12/1/2014
https://www.sparkfun.com/products/9836
SparkFun Product Page & Details for ADXL345 Breakout Board. 12/1/2014
http://ww1.microchip.com/downloads/en/DeviceDoc/41303G.pdf
Microchip PIC18F45K20 Data Sheet. 12/1/2014
http://ww1.microchip.com/downloads/en/DeviceDoc/61156H.pdf
Microchip PIC32MX69F512L Data Sheet. 12/1/2014
http://ww1.microchip.com/downloads/en/DeviceDoc/70686B.pdf
Microchip MRF24WG0MA Wi-Fi Controller. 12/1/2014
https://www.digilentinc.com/Products/Detail.cfm?NavPath=2,892,1193&Prod=CHIPKIT-WF32
Digilent ChipKit WF32 Product Page. 12/1/2014
References

## Slide 37: Product Research

## Slide 38
Device Links